## Slide 1: Inter laboratory Comparative Tests ISO 5725-2
Request from the Plant Disease Committee
Fig. 1: Conidiophores of Alternaria radicina

## Slide 2: Analyse of comparative trials
a goal to achieve
  a group of selected laboratories
  different existing techniques/methods
  a set of samples sent and analysed
a technical report including statistical analysis
  descriptive statistics
  estimate repeatability (intra laboratory) and reproducibility (inter laboratory)
  Analysis of variance + tests
  detect and analyse difference in estimate and in variability

## Slide 3: What do we need?
Agreed and accessible methods
  National and/or International norms (ISO CEN AFNOR…)
  Methods available (ANOVA, published tests,…)
Appropriate tools for the Organiser of the test
  appropriate analysis = f (data checked, goal of study)
  co-operation of various competencies
Ability to keep and re-use to (check) progress
  compare successive studies, compare to other studies
  apply different treatments on the data kept

## Slide 4
  The repeatability is a measure for the within-laboratory consistency. Pj
  (nlj – 1)S2lj
  l=1
  Repeatability variance: S2rj = 
  Pj
  (nlj – 1)
  l=1
The between-laboratory variance is a measure for variation between the participating laboratories.
S2dj - S2rj
Between-laboratory variance: S2Lj = 
  nj
  The reproducibility is the sum of repeatability and between-laboratory variance.
  Reproducibility variance: S2Rj = S2rj + S2Lj
  value = for a lab, a method, a sample; each sample analysed at least twice in a lab for a method
  ISO 5725-2 when test result = numerical value obtained or computed on a continuous scale

## Slide 5
  1 Pj
  where S2dj =  nlj(zlj - zj)2
  pj – 1 l=1
  Pj
  n2lj
  1 Pj l=1
  and nj =  nlj - 
  pj – 1 l=1 Pj
  nlj
  l=1
  l = laboratory j = method
  nlj = Number of test results obtained by laboratory l for method j
  Pj = Number of laboratories with non-missing results for method j
  Slj = Standard deviation for method j and laboratory l
  Zj = overall mean for method j 
  Zlj = mean for method j and laboratory l

## Slide 6
lab sample rep value
lab01 sple1 rep1 4.44
lab01 sple1 rep2 4.39
lab01 sple2 rep1 9.34
lab01 sple2 rep2 9.34
lab01 sple3 rep1 17.4
lab01 sple3 rep2 16.9
lab01 sple4 rep1 19.23
lab01 sple4 rep2 19.23
lab01 sple5 rep1 24.28
lab01 sple5 rep2 24
lab02 sple1 rep1 4.03
lab02 sple1 rep2 4.23
lab02 sple2 rep1 8.42
lab02 sple2 rep2 8.33
lab02 sple3 rep1 14.42
lab02 sple3 rep2 14.5
lab02 sple4 rep1 16.06
lab02 sple4 rep2 16.22
lab02 sple5 rep1 20.4
lab02 sple5 rep2 19.91
… … … ...
Type of data needed
3 to 30 laboratories
2 to XX samples
2 to 10 replicates
quantitative values
Visible on this screen:
2 labs
5 samples
2 reps

## Slide 7
Includes:
raw data, to be kept and if possible to be reproduced in extenso in report
means and variances by laboratory and by laboratory X sample
repeatability and reproducibility values
h and k values and the test of their significance

## Slide 8
h values shows if a lab has a tendency to under or over estimate
1%
1%

## Slide 9
k values indicates the relative variability of the results
!

## Slide 10
Demonstration of Access tool

## Slide 11
Interpretation of repeatability and reproducibility is not easy
a good experience on similar techniques is often necessary
Assistance from statistic(ian)s helps to point out questions to see with experts
Experts have to draw conclusions and write report
It is always interesting to have an idea from the experts of what they think is a small/big difference within and between labs; before the experiment, and after the study. This allows to design the size of the experiment (for instance nb of replicates)